## Slide 1: Linear Regression
Sarah Duclos Ivetich ETH Zurich, Institut für Chemie- und Bioingenieurwissenschaften ETH Hönggerberg / HCI F 143 E-Mail: sarah.duclos@chem.ethz.ch https://gitlab.ethz.ch/tmarcato/snm22

## Slide 2: Design of Experiments – An Example
The Problem
Measure the time (response) for pressure discharge of a tank filled with water through a pipe
Objectives
Obtain a prediction error smaller than 10%
Minimize the experimental effort
Regression factors (4)
Length of the pipe (10 – 50 m)
Diameter of the pipe (1 – 5 cm)
Head pressure (0.1 – 0.4 bar)
Temperature of water (10 – 50 ˚C)
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression

## Slide 3: Multiple Linear Regression
  Use the log10 of the discharge time
  18 experiments (based on experimental design)
  Final model (max polynomial order = 2):
Parameter | Estimate | SE | tStat | pValue
q0 | 2.9898 | 0.009 | 336.43 | 0.000
q1 | -0.2961 | 0.003 | -94.23 | 0.000
q2 | 0.1910 | 0.003 | 60.80 | 0.000
q3 | -0.9432 | 0.003 | -300.20 | 0.000
q4 | -0.0163 | 0.003 | -5.19 | 0.001
q5 | -0.0058 | 0.003 | -1.85 | 0.098
q6 | -0.0064 | 0.003 | -2.03 | 0.073
q7 | 0.0079 | 0.003 | 2.51 | 0.033
q8 | 0.4350 | 0.009 | 46.15 | 0.000
Root mean squared error (RMSE): |  |  | 0.0126 | 
R-squared: | 1.000 |  | Adjusted R2: | 1.000
F-statistic vs. constant model: |  | 13100 | p-value: | 2.24E-17
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression

## Slide 4: Model Validation
1000 experimental points randomly generated
 model under-fitting
Objective = 10%
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression

## Slide 5: D-Optimal Model Augmentation
Use the log10 of the discharge time
D-Optimal Design with 98 experiments
Final model (max polynomial order = 4):
Old model (98 exp) |  |  |  | 
Root mean squared error (RMSE): |  |  | 0.00140 | 
R-squared: | 0.9998 |  | Adjusted R2: | 0.9997
F-statistic vs. constant model: |  | 12200 | p-value: | 1.31E-115
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression

## Slide 6: Mechanistic model
Darcy–Weisbach equation
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression

## Slide 7: DoE Tank Discharge – What if no mechanistic model?
Model | Pros | Cons
Multiple Linear Regression | Very simple to start No required knowledge | Large overfitting Very large number of exps. (ca. 100)
Knowledge
No. of Experiments
Deterministic Model
Very little number of experiments (8)
Detailed knowledge required
MLR + Non-dimensional quantities (e.g. Re)
Simple to use
Little knowledge required
Not physical
Medium level of exp. effort
Limited number of experiments (15)
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression

## Slide 8
Why stepwise?
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression

## Slide 9
Are all model terms relevant for improving model performance?
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression

## Slide 10
Why validation?
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression

## Slide 11
Is developed model generally valid?
Does it perform well when I test it on an external data set?
Sarah duclos Ivetich / Numerical Methods for Chemical Engineers / Linear Regression