## Slide 1: Combinational Circuits

## Slide 2: What we will learn
Tools to build digital circuits
  Transistors
  Gates
  … and why they matter
Boolean Algebra
Combinational Circuits
Verilog

## Slide 3: Abstraction
 | Abstraction Levels | Examples
 | Application Software | Programs
 | Operating Systems | Device drivers
This Course | Architecture | Instructions, Registers
 | Micro architecture | Datapath, Controllers
 | Logic | Adders, Memories
 | Digital Circuits | AND gates, NOT gates
 | Analog Circuits | Amplifiers
 | Devices | Transistors, Diodes
 | Physics | Electrons

## Slide 4: Crash course in EE
All the good parts of EE in short
  Just the best parts, only highlights
We will have exercises where we need to put this into use
  We will use Verilog to program FPGAs…
  … and we will learn what these mean in a few hours
What do we need to know to build computers
  Understanding how they work will help you
If you want to know more
  Plenty of lectures/theses at EE (Prof. Benini, Gürkaynak)

## Slide 5: (micro)-Processors

## Slide 6: FPGAs

## Slide 7: Custom ASICs

## Slide 8: But they all look the same….
 | Microprocessors | FPGAs | ASICs
In short: | Common building block of Computers | Reprogrammable Hardware, flexible | You customize everything
Development Time | minutes | days | months
Performance | o | + | ++
Good for | Simple to use Ubiquitous | Prototyping Small volume | Mass production, Max performance
Programming | Compiler | Bitfile | Design Masks
Languages | C/C++/Java/… | Verilog/VHDL | Verilog/VHDL
Main Companies | Intel, ARM | Xilinx, Altera, Lattice | TSMC, UMC, ST, Globalfoundries

## Slide 9: But they all look the same….
 | Microprocessors | FPGAs | ASICs
In short: | Common building block of Computers | Reprogrammable Hardware, flexible | You customize everything
Development Time | minutes | days | months
Performance | o | + | ++
Good for | Simple to use Ubiquitous | Prototyping Small volume | Mass production, Max performance
Programming | Compiler | Bitfile | Design Masks
Languages | C/C++/Java/… | Verilog/VHDL | Verilog/VHDL
Main Companies | Intel, ARM | Xilinx, Altera, Lattice | TSMC, UMC, ST, Globalfoundries

## Slide 10: But they all look the same….
 | Microprocessors | FPGAs | ASICs
In short: | Common building block of Computers | Reprogrammable Hardware, flexible | You customize everything
Development Time | minutes | days | months
Performance | o | + | ++
Good for | Simple to use Ubiquitous | Prototyping Small volume | Mass production, Max performance
Programming | Compiler | Bitfile | Design Masks
Languages | C/C++/Java/… | Verilog/VHDL | Verilog/VHDL
Main Companies | Intel, ARM | Xilinx, Altera, Lattice | TSMC, UMC, ST, Globalfoundries

## Slide 11: But they all look the same….
 | Microprocessors | FPGAs | ASICs
In short: | Common building block of Computers | Reprogrammable Hardware, flexible | You customize everything
Development Time | minutes | days | months
Performance | o | + | ++
Good for | Simple to use Ubiquitous | Prototyping Small volume | Mass production, Max performance
Programming | Compiler | Bitfile | Design Masks
Languages | C/C++/Java/… | Verilog/VHDL | Verilog/VHDL
Main Companies | Intel, ARM | Xilinx, Altera, Lattice | TSMC, UMC, ST, Globalfoundries

## Slide 12: But they all look the same….
 | Microprocessors | FPGAs | ASICs
In short: | Common building block of Computers | Reprogrammable Hardware, flexible | You customize everything
Development Time | minutes | days | months
Performance | o | + | ++
Good for | Simple to use Ubiquitous | Prototyping Small volume | Mass production, Max performance
Programming | Compiler | Bitfile | Design Masks
Languages | C/C++/Java/… | Verilog/VHDL | Verilog/VHDL
Main Companies | Intel, ARM | Xilinx, Altera, Lattice | TSMC, UMC, ST, Globalfoundries

## Slide 13: But they all look the same….
 | Microprocessors | FPGAs | ASICs
In short: | Common building block of Computers | Reprogrammable Hardware, flexible | You customize everything
Development Time | minutes | days | months
Performance | o | + | ++
Good for | Simple to use Ubiquitous | Prototyping Small volume | Mass production, Max performance
Programming | Compiler | Bitfile | Design Masks
Languages | C/C++/Java/… | Verilog/VHDL | Verilog/VHDL
Main Companies | Intel, ARM | Xilinx, Altera, Lattice | TSMC, UMC, ST, Globalfoundries
Want to learn how these work
By programming these
Using this language

## Slide 14: Building Blocks For Microchips
Conductors
  Metals: Aluminum, Copper
Insulators
  Glass (SiO2), Air
Semiconductors
  Silicon (Si), Germanium (Ge)

## Slide 15: Semiconductor

## Slide 16: N-type Doping

## Slide 17: P-type Doping

## Slide 18: What Is So Great About Semiconductors?
You can “engineer” its properties
  Make it P type by injecting type-III elements (B, Ga, In)
  Make it N type by injecting elements from type-V (P,As)
Starting with a pure semiconductor, you can combine P and N regions next to each other
Allows you to make interesting electrical devices
  Diodes
  Transistors
  Thrystors

## Slide 19: The transistor
By combining
  Conductors (Metals)
  Insulators (Oxide)
  Semiconductors
We get a Transistor (MOS)
  Basically it is a switch
  Apply (positive) voltage to GATE
  Current flows from DRAIN to SOURCE
Why is this cool?
  We can combine many of these to realize simple logic gates
Gate
Source
Drain

## Slide 20: nMOS + pMOS = CMOS

## Slide 21: nMOS + pMOS = CMOS
When One Type MOS works, the other is the load

## Slide 22: CMOS Gate Structure
The general form used to construct any inverting logic gate, such as: NOT, NAND, or NOR.
  The networks may consist of transistors in series or in parallel.
  When transistors are in parallel, the network is ON if either transistor is ON.
  When transistors are in series, the network is ON only if all transistors are ON.

## Slide 23: CMOS Gates: NOT Gate
A | P1 | N1 | Y
0 |  |  | 
1 |  |  | 

## Slide 24: CMOS Gates: NOT Gate
A | P1 | N1 | Y
0 | ON | OFF | 1
1 | OFF | ON | 0

## Slide 25: CMOS Gates: NAND Gate
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 |  |  |  |  | 
0 | 1 |  |  |  |  | 
1 | 0 |  |  |  |  | 
1 | 1 |  |  |  |  | 

## Slide 26: CMOS Gates: NAND Gate
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 1
1 | 0 | OFF | ON | ON | OFF | 1
1 | 1 | OFF | OFF | ON | ON | 0
N1 and N2 are connected in series; both must be ON to pull the output to GND.
P1 and P2 are in parallel; only one must be ON to pull the output up to VDD.

## Slide 27: Common Logic Gates

## Slide 28: Moore’s Law

## Slide 29: Moore’s Law
Coined by Gordon Moore:
  In 1965
  Co-founder of Intel
Number of transistors that can be manufactured doubles roughly every 18 months.
In other words: it increases 100 fold over 10 years.

## Slide 30: How Do We Keep Moore’s Law
Manufacturing smaller structures
  Some structures are already a few atoms in size
Developing materials with better properties
  Copper instead of Aluminum (better conductor)
  Hafnium Oxide, air for Insulators
  Making sure all materials are compatible is the challenge
Optimizing the manufacturing steps
  How to use 193nm ultraviolet light to pattern 20nm structures
New technologies
  FinFET, Gate All Around transistor, Single Electron Transistor…

## Slide 31: We can now build logic circuits
A logic circuit is composed of:
  Inputs
  Outputs
Functional specification (describes relationship between inputs and outputs)
Timing specification (describes the delay between inputs changing and outputs responding)

## Slide 32: Circuits
Circuit elements
  E1, E2, E3
  Each itself a circuit
Nodes (wires)
  Inputs: A, B, C
  Outputs: Y, Z
  Internal: n1
  To count the nodes look at
    outputs of every circuit element
    inputs to the entire circuit

## Slide 33: Types of Logic Circuits
Combinational Logic
  Memoryless
  Outputs determined by current values of inputs
  In some books called Combinatorial Logic
Sequential Logic
  Has memory
  Outputs determined by previous and current values of inputs

## Slide 34: Rules of Combinational Composition
Every circuit element is itself combinational
Every node of the circuit is either
  designated as an input to the circuit or
  connects to exactly one output terminal of a circuit element
The circuit contains no cyclic paths: every path through the circuit visits each circuit node at most once
Example: (If E1-3 combinational)

## Slide 35: Boolean Equations
Functional specification of outputs in terms of inputs
Example (full adder – more later):
S = F(A, B, Cin)
Cout = G(A, B, Cin)

## Slide 36: Boolean Algebra
Set of axioms and theorems to simplify Boolean equations
Like regular algebra, but in some cases simpler because variables can have only two values (1 or 0)
Axioms and theorems obey the principles of duality:
  stay correct if ANDs and ORs interchanged and 0’s and 1’s interchanged
  Examples:
B ∙ B =
0 =

## Slide 37: Boolean Algebra
Set of axioms and theorems to simplify Boolean equations
Like regular algebra, but in some cases simpler because variables can have only two values (1 or 0)
Axioms and theorems obey the principles of duality:
  stay correct if ANDs and ORs interchanged and 0’s and 1’s interchanged
  Examples:
B ∙ B = 0
0 = 1
dual
B + B = 1
1 = 0

## Slide 38: Boolean Axioms
Duality: If the symbols 0 and 1 and the operators • (AND) and + (OR) are interchanged, the statement will still be correct.

## Slide 39: Boolean Theorems: Summary

## Slide 40: Boolean Theorems of Several Variables

## Slide 41: Simplifying Boolean Expressions: Example 2
Y = A(AB + ABC)

## Slide 42: Simplifying Boolean Expressions: Example 2
Y = A(AB + ABC)
= A(AB(1 + C)) T8
= A(AB(1)) T2’
= A(AB) T1
= (AA)B T7
= AB T3

## Slide 43: Boolean Equations Example
You are going to the cafeteria for lunch
  You won’t eat lunch
  If it is not open or
  If they only serve cabbage
Write a truth table for determining if you will eat lunch
open
only
cabb.
eat

## Slide 44: Some Definitions
Complement: variable with a bar over it , ,
Literal: variable or its complement , , , , ,
Implicant: product (AND) of literals , ,
Minterm: product (AND) that includes all input variables , ,
Maxterm: sum (OR) that includes all input variables , ,

## Slide 45: Sum-of-Products (SOP) Form
All Boolean equations can be written in SOP form
  Each row in a truth table has a minterm
  A minterm is a product (AND) of literals
  Each minterm is TRUE for that row (and only that row)
  blackboard
Formed by ORing the minterms for which the output is TRUE

## Slide 46: Sum-of-Products (SOP) Form
All Boolean equations can be written in SOP form
  Each row in a truth table has a minterm
  A minterm is a product (AND) of literals
  Each minterm is TRUE for that row (and only that row)
  blackboard
Formed by ORing the minterms for which the output is TRUE

## Slide 47: From Logic to Gates
SOP (sum-of-products) leads to two-level logic
Example:

## Slide 48: Combinational Building Blocks
Combinational logic is often grouped into larger building blocks to build more complex systems
Hide the unnecessary gate-level details to emphasize the function of the building block
We have already studied some building blocks
  full adders
  priority circuits
We now look at:
  multiplexers
  decoders

## Slide 49: Multiplexer (Mux)
Selects between one of N inputs to connect to the output.
Needs log2N-bit control input
2:1 Mux Example:

## Slide 50: Multiplexer (Mux)
Selects between one of N inputs to connect to the output.
Needs log2N-bit control input
2:1 Mux Example:
Compressed
version

## Slide 51: Hardware Description Languages
In the beginning HDLs were developed as a ‘standard way’ of drawing circuit schematics.
Modeled the interface of circuits, described how they were connected
Allowed connections between these modules
Supported some common logic functions
  AND OR NOT XOR
  Multiplexers

## Slide 52: Convenient Way of Drawing Schematics

## Slide 53: Convenient Way of Drawing Schematics
It is standard
  Everybody will interpret the schematic the same way
It is not proprietary
  HDLs are not tool specific
It is machine readable
  It is easier for computers to understand the circuit
Only later on additional benefits were discovered
  Simulation and Synthesis

## Slide 54: Two Hardware Description Languages
Verilog
  developed in 1984 by Gateway Design Automation
  became an IEEE standard (1364) in 1995
  More popular in US
VHDL (VHSIC Hardware Description Language)
  Developed in 1981 by the Department of Defense
  Became an IEEE standard (1076) in 1987
  More popular in Europe
In this course we will use Verilog

## Slide 55: Defining a module
A module is the main building block in Verilog
We first need to declare:
  Name of the module
  Types of its connections (input, output)
  Names of its connections

## Slide 56: Defining a module
module example (a, b, c, y);
input a;
input b;
input c;
output y;
// here comes the circuit description
endmodule

## Slide 57: A question of style
module test ( a, b, y );
input a;
input b;
output y;
endmodule
module test ( input a,
input b, output y );
endmodule
The following two codes are identical

## Slide 58: What if we have busses?
input [31:0] a; // a[31], a[30] .. a[0]
output [15:8] b1; // b1[15], b1[14] .. b1[8]
output [7:0] b2; // b2[7], b2[6] .. b1[0]
input clk; // single signal
You can also define multi-bit busses.
  [ range_start : range_end ]
Example:

## Slide 59: Basic Syntax
// Single line comments start with a //
/* Multiline comments
are defined like this */
Verilog is case sensitive:
  SomeName and somename are not the same!
Names cannot start with numbers:
  2good is not a valid name
Whitespace is ignored

## Slide 60: Good Practices
Develop/use a consistent naming style
Use MSB to LSB ordering for busses (little-endian)
  Try using “a[31:0]” and not “a[0:31]”
Define one module per file
  Makes managing your design hierarchy easier
Use a file name that equals module name
  i.e. module TryThis is defined in a file called TryThis.v

## Slide 61: There are Two Main Styles of HDL
Structural
  Describe how modules are interconnected
  Each module contains other modules (instances)
  … and interconnections between these modules
  Describes a hierarchy
Behavioral
  The module body contains functional description of the circuit
  Contains logical and mathematical operators
Practical circuits would use a combination of both

## Slide 62: Structural HDL: Instantiating a Module

## Slide 63: Structural HDL Example
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
Module Definitions

## Slide 64: Structural HDL Example
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
Module Definitions

## Slide 65: Structural HDL Example
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
Wire definitions

## Slide 66: Structural HDL Example
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
// instantiate small once
small i_first ( .A(A),
.B(SEL),
.Y(n1) );
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
Instantiate first module

## Slide 67: Structural HDL Example
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
// instantiate small once
small i_first ( .A(A),
.B(SEL),
.Y(n1) );
// instantiate small second time
small i2 ( .A(n1),
.B(C),
.Y(Y) );
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
Instantiate second module

## Slide 68: Structural HDL Example
module top (A, SEL, C, Y);
input A, SEL, C;
output Y;
wire n1;
// alternative
small i_first ( A, SEL, n1 );
/* Shorter instantiation,
pin order very important */
// any pin order, safer choice
small i2 ( .B(C),
.Y(Y),
.A(n1) );
endmodule
module small (A, B, Y);
input A;
input B;
output Y;
// description of small
endmodule
Short Instantiation

## Slide 69: What Happens with HDL code?
Automatic Synthesis
  Modern tools are able to map a behavioral HDL code into gate-level schematics
  They can perform many optimizations
  … however they can not guarantee that a solution is optimal
  Most common way of Digital Design these days
Simulation
  Allows the behavior of the circuit to be verified without actually manufacturing the circuit
  Simulators can work on behavioral or gate-level schematics

## Slide 70: Behavioral HDL: Defining Functionality
module example (a, b, c, y);
input a;
input b;
input c;
output y;
// here comes the circuit description
assign y = ~a & ~b & ~c |
a & ~b & ~c |
a & ~b & c;
endmodule

## Slide 71: Behavioral HDL: Synthesis Results

## Slide 72: Behavioral HDL: Simulating the Circuit

## Slide 73: Bitwise Operators
module gates(input [3:0] a, b,
output [3:0] y1, y2, y3, y4, y5);
/* Five different two-input logic
gates acting on 4 bit busses */
assign y1 = a & b; // AND
assign y2 = a | b; // OR
assign y3 = a ^ b; // XOR
assign y4 = ~(a & b); // NAND
assign y5 = ~(a | b); // NOR
endmodule

## Slide 74: Bitwise Operators: Synthesis Results

## Slide 75: Reduction Operators
module and8(input [7:0] a,
output y);
assign y = &a;
// &a is much easier to write than
// assign y = a[7] & a[6] & a[5] & a[4] &
// a[3] & a[2] & a[1] & a[0];
endmodule

## Slide 76: Reduction Operators: assign y = &a;

## Slide 77: Conditional Assignment
module mux2(input [3:0] d0, d1,
input s,
output [3:0] y);
assign y = s ? d1 : d0;
// if (s) then y=d1 else y=d0;
endmodule
? : is also called a ternary operator as it operates on three inputs:
  s
  d1
  d0.

## Slide 78: Conditional Assignment: y = s ? d1: d0;

## Slide 79: More Conditional Assignments
module mux4(input [3:0] d0, d1, d2, d3
input [1:0] s,
output [3:0] y);
assign y = s[1] ? ( s[0] ? d3 : d2)
: ( s[0] ? d1 : d0);
// if (s1) then
// if (s0) then y=d3 else y=d2
// else
// if (s0) then y=d1 else y=d0
endmodule

## Slide 80: Even More Conditional Assignments
module mux4(input [3:0] d0, d1, d2, d3
input [1:0] s,
output [3:0] y);
assign y = (s == 2’b11) ? d3 :
(s == 2’b10) ? d2 :
(s == 2’b01) ? d1 :
d0;
// if (s = “11” ) then y= d3
// else if (s = “10” ) then y= d2
// else if (s = “01” ) then y= d1 // else y= d0
endmodule

## Slide 81: How to Express numbers ?
N’Bxx
8’b0000_0001
(N) Number of bits
  Expresses how many bits will be used to store the value
(B) Base
  Can be b (binary), h (hexadecimal), d (decimal), o (octal)
(xx) Number
  The value expressed in base, apart from numbers it can also have X and Z as values.
  Underscore _ can be used to improve readability

## Slide 82: Number Representation in Verilog
Verilog | Stored Number | Verilog | Stored Number
4’b1001 | 1001 | 4’d5 | 0101
8’b1001 | 0000 1001 | 12’hFA3 | 1111 1010 0011
8’b0000_1001 | 0000 1001 | 8’o12 | 00 001 010
8’bxX0X1zZ1 | XX0X 1ZZ1 | 4’h7 | 0111
‘b01 | 0000 .. 0001 | 12’h0 | 0000 0000 0000

## Slide 83: What have seen so far:
Describing structural hierarchy with Verilog
  Instantiate modules in an other module
Writing simple logic equations
  We can write AND, OR, XOR etc
Multiplexer functionality
  If … then … else
We can describe constants
But there is more:

## Slide 84: Precedence of operations in Verilog
~ | NOT
*, /, % | mult, div, mod
+, - | add,sub
<<, >> | shift
<<<, >>> | arithmetic shift
<, <=, >, >= | comparison
==, != | equal, not equal
&, ~& | AND, NAND
^, ~^ | XOR, XNOR
¦, ~¦ | OR, NOR
?: | ternary operator
Highest
Lowest

## Slide 85: Example: Comparing two numbers
module MyXnor (input a, b,
output z);
assign z = ~(a ^ b); //not XOR
endmodule
module MyAnd (input a, b,
output z);
assign z = a & b; // AND
endmodule
An XNOR gate
An AND gate

## Slide 86: Example: Comparing Two Numbers
module compare (input a0, a1, a2, a3, b0, b1, b2, b3,
output eq);
wire c0, c1, c2, c3, c01, c23;
MyXnor i0 (.A(a0), .B(b0), .Z(c0) ); // XNOR
MyXnor i1 (.A(a1), .B(b1), .Z(c1) ); // XNOR
MyXnor i2 (.A(a2), .B(b2), .Z(c2) ); // XNOR
MyXnor i3 (.A(a3), .B(b3), .Z(c3) ); // XNOR
MyAnd haha (.A(c0), .B(c1), .Z(c01) ); // AND
MyAnd hoho (.A(c2), .B(c3), .Z(c23) ); // AND
MyAnd bubu (.A(c01), .B(c23), .Z(eq) ); // AND
endmodule

## Slide 87: Example: Comparing Two Numbers
module compare (input a0, a1, a2, a3, b0, b1, b2, b3,
output eq);
wire c0, c1, c2, c3, c01, c23;
MyXnor i0 (.A(a0), .B(b0), .Z(c0) ); // XNOR
MyXnor i1 (.A(a1), .B(b1), .Z(c1) ); // XNOR
MyXnor i2 (.A(a2), .B(b2), .Z(c2) ); // XNOR
MyXnor i3 (.A(a3), .B(b3), .Z(c3) ); // XNOR
assign c01 = c0 & c1;
assign c23 = c2 & c3;
assign eq = c01 & c23;
endmodule

## Slide 88: Example: Comparing Two Numbers
module compare (input a0, a1, a2, a3, b0, b1, b2, b3,
output eq);
wire c0, c1, c2, c3;
MyXnor i0 (.A(a0), .B(b0), .Z(c0) ); // XNOR
MyXnor i1 (.A(a1), .B(b1), .Z(c1) ); // XNOR
MyXnor i2 (.A(a2), .B(b2), .Z(c2) ); // XNOR
MyXnor i3 (.A(a3), .B(b3), .Z(c3) ); // XNOR
assign eq = c0 & c1 & c2 & c3;
endmodule

## Slide 89: Example: Comparing Two Numbers
module compare (input a0, a1, a2, a3, b0, b1, b2, b3,
output eq);
wire [3:0] c; // bus definition
MyXnor i0 (.A(a0), .B(b0), .Z(c[0]) ); // XNOR
MyXnor i1 (.A(a1), .B(b1), .Z(c[1]) ); // XNOR
MyXnor i2 (.A(a2), .B(b2), .Z(c[2]) ); // XNOR
MyXnor i3 (.A(a3), .B(b3), .Z(c[3]) ); // XNOR
assign eq = &c; // short format
endmodule

## Slide 90: Example: Comparing Two Numbers
module compare (input [3:0] a, input [3:0] b,
output eq);
wire [3:0] c; // bus definition
MyXnor i0 (.A(a[0]), .B(b[0]), .Z(c[0]) ); // XNOR
MyXnor i1 (.A(a[1]), .B(b[1]), .Z(c[1]) ); // XNOR
MyXnor i2 (.A(a[2]), .B(b[2]), .Z(c[2]) ); // XNOR
MyXnor i3 (.A(a[3]), .B(b[3]), .Z(c[3]) ); // XNOR
assign eq = &c; // short format
endmodule

## Slide 91: Example: Comparing Two Numbers
module compare (input [3:0] a, input [3:0] b,
output eq);
wire [3:0] c; // bus definition
assign c = ~(a ^ b); // XNOR
assign eq = &c; // short format
endmodule

## Slide 92: Example: Comparing Two Numbers
module compare (input [3:0] a, input [3:0] b,
output eq);
assign eq = (a == b) ? 1 : 0; // really short
endmodule

## Slide 93: What is the BEST way of writing Verilog
Quite simply IT DOES NOT EXIST!
Code should be easy to understand
  Sometimes longer code is easier to comprehend
Hierarchy is very useful
  In the previous example it did not look like that, but for larger designs it is indispensible
Try to stay closer to hardware
  After all the goal is to design hardware

## Slide 94: Parameterized Modules
module mux2
#(parameter width = 8) // name and default value
(input [width-1:0] d0, d1,
input s,
output [width-1:0] y);
assign y = s ? d1 : d0;
endmodule
We can pass parameters to a module

## Slide 95: Parameterized Modules: Instantiating
// If parameter is not given, default is assumed (here 8)
mux2 i_mux (d0, d1, s, out);
// The same module with 12-bit bus width:
mux2 #(12) i_mux_b (d0, d1, s, out);
// More verbose version:
mux2 #(.width(12)) i_mux_b (.d0(d0), .d1(d1),
.s(s), .out(out));
module mux2
#(parameter width = 8) // name and default value
(input [width-1:0] d0, d1,
input s,
output [width-1:0] y);
assign y = s ? d1 : d0;
endmodule

## Slide 96: Manipulating Bits
// You can assign partial busses
wire [15:0] longbus;
wire [7:0] shortbus;
assign shortbus = longbus[12:5];
// Concatenating is by {}
assign y = {a[2],a[1],a[0],a[0]};
// Possible to define multiple copies
assign x = {a[0], a[0], a[0], a[0]}
assign y = { 4{a[0]} }

## Slide 97: Z floating output
module tristate(input [3:0] a,
input en,
output [3:0] y);
assign y = en ? a : 4'bz;
endmodule

## Slide 98: Truth Table for AND with Z and X
& |  | A |  |  | 
 |  | 0 | 1 | Z | X
B | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 1 | X | X
 | Z | 0 | X | X | X
 | X | 0 | X | X | X

## Slide 99: What About Timing ?
‘timescale 1ns/1ps
module simple (input a, output z1, z2);
assign #5 z1 = ~a; // inverted output after 5ns
assign #9 z2 = a; // output after 9ns
endmodule
It is possible to define timing relations in Verilog
  These are ONLY for Simulation
  They CAN NOT be synthesized
  They are used for modeling delays in simulation

## Slide 100: Next Steps
We have seen an overview of Verilog
Discussed behavioral and structural modeling
Showed combinational logic constructs
Still to come: (later)
Sequential circuit description in Verilog
Developing testbenches for simulation